## Slide 1: Wildfire forecast

## Slide 2: Content
Context
Literature review
Goal definition
Data Pipeline
Model
Risk map
Conclusion and next step
Bonus: Explanaible AI? Variable importance? Parametric model for simulation

## Slide 3: Context
Wildfire are originally a necessary natural process for ecological succession and soil enhancement [1]
BUT according to Promotheus, 8 out 10 are caused by human activities [2]
Both natural conditions and human activities can enhance ignition risk and propagation, to site a few: [2]
Natural
Weather conditions (wind, rain, thunder…)
Soil moisture
Anthropologic
Accident (train, power-line…)
Malicious conduct
Vegetation types
Orographic conditions (flat, steep…)
Negligence (cigarette butt, bbq…)
Forest & farming
Urban sprawl

## Slide 4: Context
In any case, it has a powerful destructive power, and it is of paramount importance to work toward risk reduction.
3 main areas of research and application:
Prediction
Detection
Post-fire impact
Our Focus

## Slide 5: Literature reviews
Chart: Record of publications by the end of 2019 by category
| Catégorie 1
Fire occurrence, susceptibilty and risk | 127
fire detection and maping | 65
fire behavior prediction | 43
fire effects | 35
climate change | 20
fire management | 16
300 publications by the end of 2019 on ML & wildfire science (Piyush Jain & al., 2020) .
127 are related to risk analysis (lightning impact, binary classifiers, heatmap…)
Exponential growth:
Computing power
Satellite data

## Slide 6: Literature reviews
First risk mapping in 2006 (Piyush Jain & al., 2020). They used CART. Nowadays, ANN and RF are commonly used and give good results compare to linear models. (Goldarag et al. 2016, Oliveira et al. 2012)
When supervised ML, original datasets are highly imbalanced (fire/no fire) and there is no standard along the papers. If no correction, precision and F1 score are close to 0.
Often, models are evaluated on a test/evaluation set. It is interesting from a ML point of view. But for real life application we will use past and present data to predict fire occurrence without any knowledge of some parameters at t+1. (Ioannis Prapas et al. 2021, Fantine Huot et al. 2022)

## Slide 7: Goal
In that context we want to create a Proof Of Concept.
It will be a ML that will provide a risk map for the next day.
Risk will be defined as: probability a specific location will be on fire. From 0 (lowest) to 1(highest)
The Are of Interest will be around the region PACA in France.
Time granulometery will be on day.
Spatial resolution, 1km
The dataset will be balanced/imbalanced ? (TBD)

## Slide 8: Data pipeline
Density dataset
External provider
Copernicus
External provider
Terra MODIS
External provider
External provider
Remote sensoring data
Reanalysis data
Reanalysis data
Vector drawing
Personal drawing
Data cube
Raw data
raster & vector
Data providers
DataFrame
Model
Data cube building
Model building
1. Define the size
2. Request data
3. Merge
Risk Map
Deploy
Explainable AI

## Slide 9: Data cube: define the size
It is just stacking/piling over time rasters!
Latitude(217 km) * longitude (248 km) = Area Of Interest
Time = 2010/01-2021/01 (4019 days) from Lit. review
SIZE
216,286,504 tiles

## Slide 10: Collect data
Density dataset
External provider
Copernicus
External provider
Terra MODIS
External provider
External provider
Remote sensoring data
Reanalysis data
Reanalysis data
Vector drawing
Personal drawing
Raw data
raster & vector
Data providers
Population density
Meteorological data (ERA5-Land)
Fire Weather index
Area Of Interest
Vegetation (MOD13A2 v061)
Land surface temperature (MOD11A1)
Leaf Area Index (MOD15A2H v061)
Evapotranspiration (MOD16A2 v061)
Burn date (MCD64A1 v061)
Fire Mask (MYD14A2)
10 datasets
CONCLUSION
10 datasets
27 layers (features)
3 files formats
EU vs USA std. : projection, time calendar…
resolution: 500m, 1km, 9 km
Different time granulometry: hrs, days, 8, days, month

## Slide 11: Challenges
Challenge 1: It’s a lot of data
27 features * cube size
Challenge 2: we must care of the data integrity
clipping, projection, downsampling, upsampling, regridding or interpolate… A lot of transformation will be needed,
#data = 5,839,735,608
Solution: Explanatory data Analysis + features selection BEFORE merging (here)
And compare afterward

## Slide 12: Defining the Area Of Interest
Initial AOI
Missing values
50%+ in MODIS
60%+ in ERA5
7%+ Na in MODIS
19% in ERA5
More edges  More Na

## Slide 13: Defining the projection
Originally, we have data in:
  Sinusoidal projection : MODIS products
  WGS 84 (ndlr: GPS projection): ERA and Density
  Rotated pole: FWI
We will keep the WGS84 (GPS) projectionfor two main reasons
  Easier coordinate system to communicate
  Better interoperability fir practical used case and integration

## Slide 14: Features selection
High correlation between variables (same spatial location over time)
Interpretability:
  Quality data in bit signed were not useful four our study in the latest MODIS product (reanalysis)
Here the evapotranspiration “ET_500m” and the latent heat “LE_500m” flux are strongly correlated

## Slide 15: Datacube creation: python script flow
11 Create aggregated variables
Deleting duplicates attributes
Resampling to daily
Load the raw datasets
Select variables of interest
Select duration
Subset the time slice 2010-2021
Write CRS
Create CRS for sinusoidal projection, rotated pole and WGS84
Set the CRS for each dataset
Clipping
Define the Aoi
Clip to the AOI
Projection
Define a common grid
Project to the same CRS as the common grid
Project to the common grid
Create two lists
Merging
Fill the missing values
Harmonize the CF time convention to “Julian”
Subset the time slice 2010-2021
Match the coordinates
Rename the coordinates
Merge
Notes: Snippet de code à ajouter

## Slide 16: References
Piyush Jain piyush.jain@canada.ca, Sean C.P. Coogan, Sriram Ganapathi Subramanian, Mark Crowley, Steve Taylor, and Mike D. Flannigan, 2000. A review of machine learning applications in wildfire science and management
Nadeem K., Taylor S.W., Woolford D.G., and Dean C.B. 2020. Mesoscale spatiotemporal predictive models of daily human- and lightning-caused wildland fire occurrence in British Columbia. Int. J. Wildl. Fire, 29(1): 11–27.
Vega-Garcia C., Lee B.S., Woodard P.M., and Titus S.J. 1996. Applying neural network technology to human-caused wildfire occurrence prediction. AI Appl. 10: 9–18. Available from https://cfs.nrcan.gc.ca/publications?id=18949.
Goldarag Y.J., Mohammadzadeh A., and Ardakani A.S. 2016. Fire Risk Assessment Using Neural Network and Logistic Regression. J. Ind. Soc. Remote Sens. 44(6): 885–894.
Oliveira S., Oehler F., San-Miguel-Ayanz J., Camia A., and Pereira J.M. 2012. Modeling spatial patterns of fire occurrence in Mediterranean Europe using Multiple Regression and Random Forest. For. Ecol. Manage. 275: 117–129.
Fantine Huot1 , R. Lily Hu2 , Nita Goyal, Tharun Sankar, Matthias Ihme, and Yi-Fan Chen. 2022. Next Day Wildfire Spread: A Machine Learning Data Set to Predict Wildfire Spreading from Remote-Sensing Data. Available from https://arxiv.org/pdf/2112.02447.pdf
Ioannis Prapas1,2,*, Spyros Kondylatos1,2,*, Ioannis Papoutsis1 , Gustau Camps-Valls2 , Michele Ronco2 , Miguel-Ángel Fernández-Torres2 , Maria Piles Guillem2 , and Nuno Carvalhais3. 2021. Deep Learning Methods for Daily Wildfire Danger Forecasting. Available from https://arxiv.org/pdf/2111.02736.pdf

## Slide 17: Reference
Causes
[1] Earth Data from NASA
[2] Ministère de lécologie et du développement durable
Data source
Era:
era 5
What is reanalisis

## Slide 18: Manipulating